## Slide 1: Theories of Failure
Presented By-
Vineet Kumar Vashishtha
Asst. Professor
KIET Group of Institutions
Team ID: 1012_005

## Slide 2
When an engineer is select a material for the design purpose, it becomes important to calculate the state of stress that defines the material's failure. So finding the state of stress it is necessary to find the acceptable limit of material.
To prevent the material breakdown there are various theories of failure.
If the material is ductile, failure is usually specified by the initiation of yielding, whereas if the material is brittle it is specified by fracture.
Theories of Failure

## Slide 3
Maximum shear stress theory .
Maximum principal stress theory.
Maximum normal strain theory.
Maximum shear strain theory.
Maximum strain Energy theory.
Types of Theories of Failure

## Slide 4
This theory also called as Guest’s or Tresca’s or Coulomb’s theory of failure.
This theory implies that failure will occur when the maximum shear stress (τmax ) in the complex system reaches the value of maximum shear stress in simple tension at the elastic limit. i.e.
Maximum shear stress theory

## Slide 5
In actual design (σet ) in above equation is replaced by the safe stress. This theory give quite satisfactory results for ductile materials.
Maximum shear stress theory

## Slide 6
This theory also called as Rankine’s theory of failure.
This theory implies that failure will occur when the maximum principal stress (σ1) in the complex system reaches the value of maximum stress in simple tension at the elastic limit (σet).Or the minimum principal stress reaches the elastic limit stress (σec) in simple compression.
Maximum Principal stress theory

## Slide 7
means numerical value of
This theory gives suitable results for brittle materials.
Maximum Principal stress theory

## Slide 8
This theory also called as Saint Venant’s theory of failure.
According to this theory failure will occurs when the maximum principal tensile strain (e1) reaches the value of maximum strain at the elastic limit in simple tension or the minimum principal strains (e3) reaches the value of maximum stress at the elastic limit in simple compression.
e1 = 1/E [σ1 - µ (σ2+ σ3 )]
e3 = 1/E [σ3 - µ (σ1+ σ2 )]
Maximum Normal strain theory

## Slide 9
Conditions to failure
e1≥ σet/E ,in simple tension
e3≥ σec/E ,in simple compression
[σ1 - µ (σ2+ σ3 )] ≥ σet
[σ3 - µ (σ1+ σ2 )] ≥ σec
Maximum Normal strain theory

## Slide 10
According to this theory failure of a material occurs when the shear stain energy per unit volume in the stresses material reaches a value equal to the shear stain energy per unit volume of the material at the elastic limit. in simple tension.
1/12C [ (σ1 - σ2 ) 2 + ( σ2 - σ3 ) 2 + (σ3 - σ1 ) 2 ]} ≥
2σet 2 /12C
Maximum Shear strain theory

## Slide 11
This theory also called as Distortion or Von mises – Hencky theory of failure.
(σ1 - σ2 ) 2 + ( σ2 - σ3 ) 2 + (σ3 - σ1 ) 2 ≥ σet 2
For two dimensional
σ2 =0
{σ1 2 + σ3 2 - [ (σ3 σ1 ) ]} ≥ σet 2
Maximum Shear strain theory

## Slide 12
Maximum Shear strain theory

## Slide 13
According to this theory failure of a material occurs when the total stain energy in the material reaches the total stain energy of the material at the elastic limit in simple tension
1/2E {σ1 2 + σ2 2 + σ3 2 - 2 µ[ (σ1 σ2 ) ( σ2 σ3 ) (σ3 σ1 ) ]} ≥
σet 2 / 2E
{σ1 2 + σ2 2 + σ3 2 - 2 µ[ (σ1 σ2 ) ( σ2 σ3 ) (σ3 σ1 ) ]} ≥ σet2
For two dimensional
σ2 =0
{σ1 2 + σ3 2 - 2 µ[ (σ3 σ1 ) ]} ≥ σet 2
Maximum strain Energy theory

## Slide 14
Maximum strain Energy theory

## Slide 15
References
Strength of Materials by R. K. Rajput
Strength of Materials L. Singer
Advanced Strength of Materials by Alok Gupta

## Slide 16: Thank You